## Slide 1
In Silico Estimation of the Performance of Transcutaneous CO2 Sensors for Detecting Hypercapnia in Newly Admitted Inpatients
Dustin M Anderson-Bell MD1, Brian W Locke MD MSc2
1: University of Utah Health, Division of Pulmonary and Critical Care; 2: Intermountain Medical Center, Division of Pulmonary and Critical Care
RESULTS
INTRODUCTION
- Detecting elevated arterial CO₂ (PaCO₂) is key for studying
hypercapnic respiratory failure.
- Arterial blood gas (ABG) is the gold standard but is invasive
and may bias patient participation.
- Transcutaneous CO₂ (TcCO₂) sensors could offer a
noninvasive solution.
- We simulated TcCO₂ measurement accuracy using existing
error estimates (Conway et al., 2017) to evaluate potential
for identifying hypercapnia in hospitalized adults.
METHODS
- Population: ABGs drawn on admission (Jan 1–Dec 31, 2022) from the TriNetX network (~115 million patients across the U.S.).
- Simulation:
1) Estimated TcCO₂ = PaCO₂ + 0.09 mmHg bias ± 4.60mmHg
2) Classified outcomes:
  - True Positive: PaCO₂ > 45mmHg and TcCO₂ > 45mmHg
  - False Positive: PaCO₂ ≤ 45mmHg and TcCO₂ > 45mmHg
  - True Negative: PaCO₂ ≤ 45mmHg and TcCO₂ ≤ 45mmHg
  - False Negative: PaCO₂ > 45mmHg and TcCO₂ ≤ 45mmHg
- Outcomes: Sensitivity, specificity, predictive values.
LIMITATIONS
- Patients receiving ABGs may have more extreme PaCO2
derangements than those without ABGs
- Disagreement between TcCO2 and PaCO2 may be non- Gaussian.
- The accuracy of TcCO2 for binary classification of
hypercapnia is likely high as many admitted patients have
PaCO2 values sufficiently far from the threshold to make
classification errors unlikely.
-
TcCO2 may offer a useful tool to identify hypercapnia
noninvasively among hospitalized adults.
CONCLUSIONS
This work is supported by grants from the American Thoracic Society (ASPIRE fellowship), the Intermountain Fund, and the National Institutes of Health (Ruth L. Kirschstein National Research Service Award 5T32HL105321 and National Center for Advancing Translational Sciences Award UM1TR004409 )
ACKNOWLEDGEMENTS
- 158,228 ABGs were included (57.8% critical care, 54.9% male, 35.3% ventilated, 65.4% non-Hispanic white, 14.4% Black)
- Mean PaCO2: 42.6 ± 17.3 mmHg; (> 45 mmHg in 30.3% of cases.
- Simulated test characteristics:
- Sensitivity: 84.2%
- Specificity: 91.0%
- Negative predictive value: 93.0%
- Positive predictive value: 80.4%
 | PaCO₂ Abnormal (≥45 mmHg) | PaCO₂ Normal (<45 mmHg) | Total | 
TcCO₂ Positive (≥45 mmHg) | 40,423 | 9,881 | 50,304 | PPV = 80.4%
TcCO₂ Normal (<45 mmHg) | 7,572 | 100,352 | 107,924 | NPV = 93.0%
Total | 47,995 | 110,233 | 158,228 | 
 | Sens = 84.2% | Spec = 91.0% |  | 
Notes: Preparing your poster for printing:
Go to File > Save As. Under Save as type (Windows) or Format (OS X), select PDF.
Open the PDF in Adobe Photoshop. Go to File > Save As. Under Format, select JPEG or TIFF. Choose a location and file name for your file and click Save. Click OK on the default save settings.
DO NOT SAVE TO A JPEG OR TIFF FROM POWERPOINT!
48 inches wide X 36 inches high