## Slide 1
Is an Arterial Blood Gas Necessary to Detect Hypercapnia?
An In-Silico Simulation of Transcutaneous CO2 to Identify Hypercapnia
Dustin M Anderson-Bell MD1, Brian W Locke MD MSc2
1University of Utah Health, Division of Pulmonary and Critical Care. 2Intermountain Medical Center, Department of Pulmonary and Critical Care
INTRODUCTION
Problem: Accurate detection of elevated arterial CO₂ (PaCO₂) is essential for studying hypercapnic respiratory failure.
Gap: Requiring ABG sampling may deter research participation. The operating characteristics of non-invasive transcutaneous CO₂ (TcCO₂) sensors are uncertain.
Objective: To simulate TcCO₂ accuracy for detecting hypercapnia using published TcCO2-PaCO2 agreement estimates (Conway et al., 2019) among patients who underwent ABG sampling in a national sample.
METHODS
LIMITATIONS
Patients who undergo ABG sampling may have more extreme PaCO2 values than those who don’t, thus inflating sensitivity/specificity.
TcCO2-PaCO2 agreement assumed to be Gaussian, but anomalous outlier disagreements may occur in practice.
Among patients currently receiving ABG sampling, TcCO₂ would accurately identify those with hypercapnia. Few PaCO₂ measurements fall into a borderline range where the known disagreement between TcCO₂ and PaCO₂ would change the classification of hypercapnia.
Next steps:
Simulated accuracy in specific subgroups (by comorbidities, by setting of care)
Propensity weighting to estimate performance in patients without ABG results
CONCLUSIONS
Conway et al. Accuracy and precision of transcutaneous carbon dioxide monitoring: a systematic review and meta-analysis. Thorax, 74(2), 157-163 (2019) & STATA analytic code
DATA ACCESS
RESULTS
Supported by
The American Thoracic Society ASPIRE fellowship
The Intermountain Foundation
The National Institutes of Health: Ruth L. Kirschstein NRSA 5T32HL105321 and
  NCATSs Award UM1TR004409
Notes: Preparing your poster for printing:
Go to File > Save As. Under Save as type (Windows) or Format (OS X), select PDF.
Open the PDF in Adobe Photoshop. Go to File > Save As. Under Format, select JPEG or TIFF. Choose a location and file name for your file and click Save. Click OK on the default save settings.
DO NOT SAVE TO A JPEG OR TIFF FROM POWERPOINT!
48 inches wide X 36 inches high

## Slide 2
-
Sensitivity, Specificity, and PPV/NPV of TcCO2 for Hypercapnia
76 medical centers with 115 million patients
TriNetX database
All database encounters between 01/01/2022 – 12/31/2022 with an ABG on admission
197,698 ABGs
(58% critical care, 55% male, 35% ventilated, 65% non-Hispanic white, 14% Black)
POPULATION
SIMULATION
OUTCOME
Simulated TcCO₂ = PaCO₂ + 0.09mmHg bias ± 4.60mmHg
Mean = 42.6 ± 17.3 mmHg
(30% > 45 mmHg)
1 simulated TcCO2 created for each PaCO2 based on Conway et al. estimates of mean bias, within-patient/within-study variance, between-study heterogeneity in bias estimates, and sampling uncertainty

## Slide 3
Simulated TcCO₂ = PaCO₂ + 0.09mmHg bias ± 4.60mmHg
Mean = 42.6 ± 17.3 mmHg
(30% > 45 mmHg)
Notes: Code for graph:
* Create first histogram and save it
clear
set obs 1000
gen PaCO2 = rnormal(42.6, 17.3)
histogram PaCO2, bin(20) normal color(navy) ///
xscale(range(10 100)) xlabel(10(10)100) ///
title("Distribution of PaCO₂ from TriNetX") ///
name(hist1, replace)
* Create second histogram and save it
clear
set obs 1000
gen TcCO2 = rnormal(50, 17.3)
histogram TcCO2, bin(20) normal color(maroon) ///
xscale(range(10 100)) xlabel(10(10)100) ///
title("Simulated Distribution of TcCO₂") ///
name(hist2, replace)
* Combine the two graphs side-by-side
graph combine hist1 hist2, cols(2)

## Slide 4
 | TcCO₂ Abnormal (≥45 mmHg) | TcCO₂ Normal (<45 mmHg) | Total | 
PaCO₂ Positive (≥45 mmHg) | 53,120 | 7,460 | 60,580 | PPV = 90.9%
PaCO₂ Normal (<45 mmHg) | 5,165 | 131,953 | 137,118 | NPV = 94.5%
Total | 58,285 | 139,953 | 197,698 | 
 | Sens 87.4% | Spec = 96.1% |  |